## Slide 1: Machine Learning for Electrode Motion Removal in EGC signals.
Ben Russell

## Slide 2: Project Objective
Electrocardiographs (ECG’s) can be corrupt with 4 primary sources of noise:
Noise Source | Typical Frequency Range (Hz)
Baseline Wander | 0.1 – 1
Electrode Motion | 1 – 10
Powerline Interference | 50 / 60
Muscle Artefact | 10 - 1000
A typical ECG signal contains frequency components between 1 and 50 Hz.
Electrode Motion, Powerline Interference and Muscle artefact can all overlap with the frequency spectrum of an ECG.
This leads to distortion.
To remove distortion, digital filters can be used to minimize noise.
However, digital filters are typically only effective if the noise is linear and stationary.
Electrode Motion and Muscle Artefact are non-linear and non-stationary.
Electrode Motion directly overlaps with the P, QRS, and T waves, making it extremely difficult to remove with traditional filters.

## Slide 3: Work Done to date
A reference database has been created with the following objectives:
  ECG signals completely devoid of noise are generated. These will act as a ground truth.
  ECG signals are corrupt with Electrode Motion noise.
  The clean signals contain a large variation of morphologies. This refers to the shape of the P wave, QRS complex, T-Wave and Heart Rate.
  There is a large variation of noise signals that are being added to the signal.

## Slide 4: Plan for the remainder.
Using the reference dataset, train both Machine Learning and Deep Learning models to learn the characteristic shape of noise signals.
Use the model to remove noise from noise corrupt ECG signals.